## Slide 1: Life-cycle assessment of food systems methods, tools and databases
Workshop of the Data Science Initiative for Africa (DSI-A) Training Programme, Durban, 10 July 2023 Bernd Franke and team

## Slide 2: Part 1: Life Cycle Assessment (LCA)

## Slide 3: Product LCA - Definition
Life Cycle Assessment is a compilation and evaluation of the inputs, outputs and the potential environmental impacts of a product system throughout its life cycle
–ISO 14040
“

## Slide 4: LCA Framework according to ISO 14040/44

## Slide 5: Life Cycle Impact Assessment in LCA
Activities
CO2
CH4
N2O
SO2
NH3
NOx
SF6
NH4
Inventory
Classification
Impact Categories
Global Warming
Acidification
Eutrophication
…
Characterization
Impact Indicator
Global Warming Potential
CO2-equivalents
Acidification Potential
SO2-equivalents
Eutrophication Potential
PO4-equivalents
Notes: All icons are public domain

## Slide 6: Life Cycle Impact Assessment in LCA

## Slide 7: Standards and Guidelines (1)

## Slide 8: Standards and Guidelines (2)

## Slide 9: System boundaries: food system vs. beverage container

## Slide 10: Direct land use change (dLUC)

## Slide 11: Indirect land use change (iLUC)

## Slide 12: Apples

## Slide 13: Apples: life cycle scenarios

## Slide 14: Apples life cycle: results

## Slide 15: Apples life cycle: sensitivity assessment

## Slide 16: Lettuce

## Slide 17: Lettuce: life cycle scenarios

## Slide 18: Lettuce: life cycle results

## Slide 19: Conclusions: Apples and Lettuce
Regional and seasonal production is advantageous if production systems are similar
Regional but not seasonal products
  Tend to be advantageous even if cooled storage over 6 month is needed
  Tend to be disadvantageous if heating is needed
Recommendation: regional and seasonal

## Slide 20: Beef
Bildchen

## Slide 21: Beef: life cycle scenarios

## Slide 22: Beef: life cycle scenario results

## Slide 23: Conclusions: beef
Regional production is advantageous with regard to GHG emissions
Advantages and disadvantages are more cause by differences in livestock production systems than by transport distances
GHG Emissions per kg of beef are about 20 times higher compared to GHG emissions per kg of apples or lettuce

## Slide 24: Bread

## Slide 25: Bread: life cycle scenarios

## Slide 26: Bread: life cycle results

## Slide 27: Consumer phase (shopping)
(Matty Symons © www.fotolia.de)

## Slide 28: GHG emissions from shopping

## Slide 29: Supply chain losses

## Slide 30: Packaging
MJ PE / l

## Slide 31: Six reasons for the variation in food LCAs

## Slide 32: CO2, land use and phosphate rock footprints
The land use and phosphate rock footprints can be quite different to the CO2 footprint of a food product.

## Slide 33: Conclusions (1)
Regional production is advantageous if the productions systems are the same.
If production systems differ:
For vegetables and fruits:
Non-seasonal vegetables are most likely disadvantageous if heating is needed.
Non-seasonal vegetables/fruits can still be advantageous is only cooled storage is needed.
For beef:
No recommendation (depending on production system, opposing effects on energy and climate)
Much higher GHG emission compared to vegetables/fruits (about 20 times per kg)
For bread:
Industrial bakery more energy efficient. But: Only for low consumer transport distances.

## Slide 34: Conclusions (2)
If regional production is advantageous or not depends on the production system
Regional processing is often small-scale processing and can be less energy efficient
Productions system for some products can be very different in different regions
Seasonality: Regional, non-storable products are advantageous only as seasonal products
Cooled storage can be more efficient than intercontinental supply of fresh commodities

## Slide 35: Conclusions (3)
Recommendations to consumers
Regional + seasonal
Don’t go shopping by car (or don’t drive extra kilometers)
Buy only what you can eat
Analysis of specific production chains may be necessary
Recommendation to retailers
Regional + seasonal ingredients
Optimization of food supply chain: Minimum losses
Optimization of processing (energy efficiency)

## Slide 36: Limitations
Results relate to GHG emissions only
Other environmental effects not regarded, such as
Impact on biodiversity
Eutrophication and acidification
Water use (addressing scarcity)
Land use
Phosphate use
Social implications not regarded

## Slide 37: Group work (4 groups @ 4-5 persons)
Group work (20 minutes)
Select a question related to LCA of food in your geographical area
Define the scope of the LCA
Define system boundary
Define life-cycle steps
Describe the necessary data collection
Report back of group work (10 minutes)

## Slide 38: Part 2: Tools and Databases
LCA Tools
Open LCA
Commercial tools (Gabi, SimaPro, Umberto etc.)
Databases for food LCA
FAO Stat
World Resources Institute (WRI)
Bilan Carbone (French)
Integrated Urban Planning with the Rapid Planning Simulator
Tools for GHG balances of hospitals
Healthcare Without Harm: Climate Impact Checkup Tool
Ecocockpit GHG balance of the Heidelberg University Hospital

## Slide 39: LCA Software

## Slide 40: Databases
● ecoinvent – 11,000 data sets, focus on Europe, very consistent, well documented, subject to a fee.www.ecoinvent.org
● GaBi Databases – 7,000 data records from Thinkstep (formerly: PE international), subject to a fee with a few exceptions http://www.gabi-software.com/deutsch/databases/
● ProBas (German) – 8,000 data records of different quality, focus on energy, materials & products, transport, disposal, German Federal Environment Agency, free of charge. www.probas.umweltbundesamt.de
● NREL – Focus US, free. www.lcacommons.gov/nrel
● Many other mostly thematically specialized databases (BioEnergieDat, ÖkoBauDat, NEEDS, LCAFood, ...) Some of them listed here: https://nexus.openlca.org/databases

## Slide 41: Open LCA https://www.openlca.org/

## Slide 42: FAO Stat https://www.fao.org/faostat/en/#compare

## Slide 43: FAO Stat

## Slide 44: FAO Stat

## Slide 45: World Resources Institute (WRI) - https://www.wri.org/food
World Resources Institute (WRI)

## Slide 46: Bilan Carbone https://www.climfoot-project.eu/en/bilan-carbone%C2%AE-clim%E2%80%99foot-tool
Tool
Database (Excel spreadsheet)
14080 lines, 67 columns

## Slide 47
Duration: 2014-2019 Funding: German Ministry of Education and Research BMBF Partner cities: Kigali Danang/Vietnam Assiut/Egypt

## Slide 48: Rapid Planning - Overview

## Slide 49
Rapid Planning provides …
Information by satellite images
Socio-economic data
Data and information on sectoral infrastructure
Specific planning values
Scenario definition
culminate into
Rapid Planning Simulator
Stakeholder involvement, planning processes
System understanding
Capacity building
supports
Visions and ideas, inspired also by “Entry projects”
Scenario definition
Rapid Planning - Scenario simulation

## Slide 50
Spatial Units
(e.g. City districts)
Water
Wastewater
Energy
Waste
Food/Agriculture
Extract of RP-Simulator block library
Rapid Planning – build a model of your city

## Slide 51: Rapid Planning – Example: Module „Constructed Wetland“
Constructed Wetland
https://www.ots.at/
https://www.energieagentur.nrw

## Slide 52
Primary Agriculture - wetlands
Rapid Planning – Example: Module „Agriculture“
Primary Agriculture - hillsides
Secondary Agriculture
Primary Agriculture - wetlands
Secondary Agriculture - wetlands

## Slide 53
Here: Trans-sectoral scenario
Output data:
Flows, concentrations of each flux in the system
Environmental information:
  Greenhouse Gas emissions, …
  Energy consumptions
Area demands
Import needs, ……
Rapid Planning – Scenario simulation for Kigali

## Slide 54
Rapid Planning – Scenario simulation for Kigali

## Slide 55: Emission Categories in the Greenhouse Gas Balance of Companies According to the Greenhouse Gas Protocol
Scope 1: Emissions from sources that belong to the company (e.g. heating vessels, vehicles)
Scope 2: Emissions from use of purchased energy (e.g. electricity, heat, cooling)
Scope 3: Emissions from activities outside the company (e.g. purchase of products or sercices, commuting of personnel, waste management)
Source: https://ghgprotocol.org/sites/default/files/standards/Scope3_Calculation_Guidance_0.pdf

## Slide 56: Mapping GHG Emissions – Hybrid Methodology
Sources: ADEME, Eurostat
Top-Down Balance Input-Output tables link economic and GHG emission data (e.g. pharmaceuticals, medical products)
Bottom-Up Balance GHG emissions calculated based on consumption data using emission factors (e.g. electricity, fuel, anesthetics)
z.B. pharmaceuticals : 296 t CO2-eq per million €
z.B. electricity (Germany): 0.48 kg CO2-eq per kWh
Notes: The organizational boundaries define if an emission source is scope 1+2 or 3

## Slide 57: Healthcare Without Harm: Climate Impact Checkup Tool

## Slide 58: GHG-Balance for the Heidelberg University Hospital ecocockpit

## Slide 59: GHG-Balance for the Heidelberg University Hospital in 2019 Values in tonnes (Mg) of CO2-eq
Scope | t CO2-eq/a | Share
Scope 1 | 6,600 | 2.9 %
Scope 2 | 50,300 | 21.0 %
Scope 3 | 172,500 | 75.2 %
Summe | 229,400 | 100 %
Scope 2
Scope 3
Scope 1
13.423 employees (2019) -> 17 t CO2-eq per employee and year Turnover 2019: 1.3 bln € -> 180 t CO2-eq per million €

## Slide 60: Group work (10 teams @2 persons)
Group work (15 minutes)
Search for GHG emission factors for at least three food types - one vegetable or fruit - one meat or dairy product - one complete meal
Use Google search
Search in Base carbone Excel sheet Base Carbone - données V18.1.xlsx
Search for data in https://www.wri.org/food
Report back about results (15 minutes)

## Slide 61: Thanks for your attention. Questions?
Bernd Franke and Team (bernd.franke@ifeu.de)